## Slide 1: Hazardous Waste Management
Office of Environmental Health and Safety
University of Alabama at Huntsville
2014

## Slide 2: Objectives
To demonstrate the proper methods of laboratory hazardous waste management for compliance with state and federal regulations.
To provide accident management and spill clean-up procedures

## Slide 3: Training Topics
Regulations
Define Hazardous Waste
Container Management
Waste Labeling
Waste Compatibility
Storage Area management
Waste Minimization
Waste- Pickup
Spill Clean-up

## Slide 4: Who Regulates Hazardous Waste?
Environmental Protection Agency (EPA)
  Regulates all aspects of hazardous waste
Department of Transportation (DOT)
  Regulates hazardous waste transportation
Department of Homeland Security (DHS)
  Regulates security threats associated with chemicals.

## Slide 5: Resource Conservation and Recovery Act: RCRA
Protecting human health and the natural environment from the potential hazards of waste disposal.
Reducing the amount of waste generated, through source reduction and recycling
Ensuring the management of waste in an environmentally sound manner.
"Cradle to Grave" requirements: Hazardous waste is regulated from the moment it is created through the time of final disposal. Generator is forever responsible for their waste.

## Slide 6: RCRA
Under the Resource Conservation and Recovery Act (RCRA), EPA regulates individuals who generate & accumulate hazardous wastes.
All labs, studios, and shops that accumulate hazardous wastes are subject to unannounced inspections by Alabama Department for Environmental Management(ADEM) and/or EPA and can be fined.

## Slide 7: Responsibilities of UAH
EPA views UAH as a hazardous waste generator
Generators are responsible for:
  properly identifying hazardous waste
  proper management of hazardous waste
    Use
    Storage
    Disposal

## Slide 8: Most Common EPA Violations
Most commonly cited EPA violations of hazardous waste regulations are:
  Open containers or lids not screwed on tight
  Improper labels/identification
  Lack of secondary containment for leaks
  Wastes from multiple locations consolidated in one room
The 4L’s – Lids, Leaks, Labels and Location

## Slide 9: EPA Fines for Non-compliance
The EPA does impose fines against universities and colleges
Examples include:
  UAH - $25,000
  Boston University - $800,000
  Penn State - $1 million
  UC Berkeley - $1 million
  Stanford University - $1 million

## Slide 10: What is a hazardous waste?
Hazardous waste is waste that is dangerous or potentially harmful to our health or the environment.
Hazardous wastes can be liquids, solids, gases, or sludge.
They can be discarded commercial products, like cleaning fluids or pesticides, or the by-products of manufacturing processes.
Hazardous waste are divided into:
    Listed wastes
    Characteristic wastes

## Slide 11: Listed and Acutely Toxic Waste
EPA-listed wastes:
F-list: This list identifies wastes from common manufacturing and industrial processes, such as solvents that have been used in cleaning or degreasing operations
K-list (source-specific wastes). This list includes certain wastes from specific industries, such as petroleum refining or pesticide manufacturing
P-list and the U-list (discarded commercial chemical products). These lists include specific commercial chemical products in an unused form.
All EPA P-listed wastes are acutely toxic

## Slide 12: Characteristic Waste
Ignitable
Corrosive
Reactive
Toxicity

## Slide 13: Ignitable
A liquid with a flash point below 60o (140oF)
A non-liquid, which under standard conditions is capable of causing fire through friction, absorption of moisture, or spontaneous chemical changes
An ignitable compressed gas
An oxidizer, such as permanganate, inorganic peroxide, or nitrate
Examples include ethanol, sodium nitrate, hydrogen gas, xylene and acetone

## Slide 14: Reactivity Characteristic
A waste is reactive if it meets any of the following criteria:
    It can explode or violently react when exposed to water or under normal handling conditions
    It can create toxic fumes or gases when exposed to water or under normal handling conditions
    Examples include sodium metal, reactive sulfides, potassium cyanide and picric acid

## Slide 15: Corrosive and Toxic Characteristic
The corrosivity characteristic identifies wastes that are acidic or alkaline (basic). Such wastes can readily corrode or dissolve flesh, metal, or other materials.
Liquid with a pH less than or equal to 2 or a pH greater than or equal to 12.5. Examples: hydrochloric acid, glacial acetic acid
A Toxic waste is a material that can be harmful or fatal if you are exposed and can pollute groundwater if released on land. Toxic wastes are listed by EPA. There are currently 40 contaminants on the list that include certain heavy metals, pesticides and organic compounds. Examples: lead-based paints, cadmium, arsenic

## Slide 16: Hazard Symbols

## Slide 17: Peroxide Formers and Time Sensitive Chemicals
Some chemicals if stored too long can produce organic peroxides capable causing explosions under heat or friction. The unusual stability problems of this class of compounds make them a serious fire and explosion hazard.
Examples:
    Ethers
    Tetrahydrofuran
    Picric/Picrylsulfonic Acid

## Slide 18: How to Handle Peroxide Formers?
Do Not Attempt to Open Expired Peroxide Formers
Time-Sensitive Chemicals
Check for crystallization periodically
Dispose of no later than 12-18 months after purchase
Call OEHS #2171 to pick up all expired chemicals

## Slide 19: Reactive Chemicals
Old or expired reactive chemicals can be potentially dangerous
Peroxide formers such as ether should not be handled
Notify OEHS immediately if found in your lab

## Slide 20: Who makes the Hazardous Waste Determination?
Environmental Health & Safety has the final determination of whether a waste is hazardous and its proper disposal.
Therefore, all accumulated chemical wastes should be treated as hazardous wastes.
No Chemical Wastes Down The Drain or in the Trash!
Dilution is not the pollution solution.
Contact OEHS for waste pick-up

## Slide 21: If unsure whether the waste created is hazardous:
Consult your supervisor.
Consult with EPA Waste lists.
Refer to the products Material Safety Data Sheet.
Contact the Environmental Health and Safety Office # 2171

## Slide 22: Container Management
Chemical waste must be stored in containers (including lids) composed of materials that are compatible with the waste.
Chemical waste containers must be in good condition and free of leaks and residue on the outside of the container.
Keep containers closed at all times except when adding or removing contents. Evaporation of wastes is a violation.
For liquids, fill containers to about 90% of container volume. Do NOT fill containers to the top. Leave at least 2 inches of space in liquid waste containers to allow for liquid expansion and decanting.

## Slide 23: Container Management
  Flammable liquids – original manufacturers or UL listed containers
  Concentrated acids or bases-Original containers, or 2.5 Liter ‘acid’ safety bottles
  Solid waste – Plastic high density polyethylene bottles
  Aqueous waste-glass bottles or HDPE plastic bottles
  Milk jugs, soda bottles and food containers unacceptable.

## Slide 24: Closing Chemical Waste Containers
Chemical waste containers must be tightly closed to prevent leakage or spillage.
Containers should be closed with a screw-type lid or other appropriate device.
Plastic wrap, aluminum foil, parafilm and other temporary lids are unacceptable.
A container holding chemical waste must ALWAYS be closed, except when waste is actually being added.
If a waste container is used to collect waste from a continuous process (i.e., drainage from a process collected with tubing inserted into a bottle such as HPLC), the container must still be sealed using rubber stoppers with tubing inserts or other appropriate means. It is not acceptable to leave funnels in chemical waste containers.

## Slide 25: Example – Open Containers
A funnel is not a lid!
Lid open when not in use

## Slide 26: Chemical Waste Labeling
All chemical waste containers must be have yellow chemical waste label affixed on the bottle
  Available from OEHS
The following information must be provided on the label (see example of the label later in this section):
    PI Name or Generator name
    Building
    Room number
    Telephone number
    Exact contents of the container

## Slide 27: Yellow Waste Label

## Slide 28: Satellite Accumulation Area: SAA
A specific area should be designated in the laboratory as a chemical waste storage area. The area must be marked with “Waste Storage Area” signage (available with OEHS and Department Office)
Waste must be stored in the room it was generated in and cannot be transferred to any area that requires passage through a door.
Chemical waste must be stored with secondary containment so that spills cannot reach sinks, or floor drains.
Incompatible chemical wastes must be segregated to prevent reaction.

## Slide 29: Satellite Accumulation Area: SAA
Satellite Accumulation Area (SAA)
- At or near the related work process
- Under the control of the generator
- Maximum amount stored 55 gallons or 1
quart acutely hazardous
Secondary containment and weekly inspections are strongly recommended.

## Slide 30: Segregation of Waste at SAA
Separate by hazards
  flammable
  toxic
  corrosive
  reactive
Separate by distance and containment.

## Slide 31: SAA Warning Signs

## Slide 32: SAA management
Waste containers stored in a SAA must be:
  In good condition
  Compatible with the waste being stored
  Kept closed at all times except when filling
  Labeled with a yellow chemical waste label from OEHS
  Stored inside secondary containment bins
Original containers of unused materials do not need a waste label if the original label is clearly legible
  Waste must always remain in the lab
  Never store waste in PUBLIC AREAS (such as hallways)

## Slide 33: Clean SAA

## Slide 34: Mixing Waste
  Divide wastes into separate waste streams
  Acids Bases
  Oxidizers Solids
  Photographic waste Mercury

## Slide 35: Mixing Chemical Waste
Mixing a hazardous waste with a non-hazardous waste may increase the volume of hazardous waste for disposal or increase disposal costs due to differences in disposal options for certain hazardous wastes.
DO NOT mix incompatible materials in the same container.
Consult with OEHS prior to mixing different chemical wastes.

## Slide 36: Mixing Hazardous Waste
  Solvents should be separated where possible as halogenated (chloroform and methylene chloride) and nonhalogenated waste (propanol, methanol, and toluene).
  Inorganic wastes containing barium, lead and cadmium may be mixed together.

## Slide 37: Empty Containers
A container of a non-acute hazardous waste, other than a pressurized cylinder, is empty if:
All wastes have been removed that can be removed through, and
    If the container is less than or equal to 119 gallons no more than one inch of residue remains on the bottom of the container, or no more than 3 percent by weight of the total capacity of the container remains;
    A compressed gas cylinder that contained hazardous material is empty when the pressure in the container approaches atmospheric pressure.
Empty plastic and brown glass chemical containers may be rinsed with water and disposed of in a sealed box with trash. Caps must be removed and labels must defaced and marked “EMPTY”.

## Slide 38: Empty Containers of Acutely Hazardous Waste
Empty containers that contained acutely hazardous wastes are managed as hazardous wastes

## Slide 39: NON-HAZARDOUS WASTE
Materials that are not considered hazardous waste must be disposed as solid waste.
Empty containers must have the labels defaced or removed.
Paper products that are not saturated with hazardous materials and/or biomedical waste can be disposed as non-hazardous waste.
Broken glass and pipettes must be placed in a broken glass rigid disposal container.

## Slide 40: Sharps Disposal
Sharps containers for disposal of these items should be conveniently located and easily accessible in all work places where sharps are used.

## Slide 41: Waste Minimization
Practice the concept of Source Reduction by simply ordering the smallest quantity of chemical materials
Keep an inventory of chemicals on hand.
Share surplus chemical with other labs.
Purchase mercury-free instruments.
Substitute hazardous chemicals with non-hazardous chemicals whenever possible.
Reduce the scale of laboratory experiments to reduce the volume of waste being produced whenever possible.

## Slide 42: Waste Pick-up
Picked up by OEHS per specific building schedule or by request.
The Chemical Disposal Inventory Form must accompany all waste and surplus chemicals.
Waste containers must be stored for pick up in the room in which they were generated
Chemical wastes must NOT be disposed of by evaporation. This includes evaporation in fume hoods or biosafety cabinets.
It’s free!!!!

## Slide 43: Waste Inventory Sheet
Chemical Name | Number of Containers | Size of Containers | Chemical Suitable for Reuse/Exchange Y/NO | Special hazards
Total number of containers on page: |  |  |  | 

## Slide 44: On-Site Hazardous Materials Management
Annual review of chemicals
Removal of surplus chemicals and chemical waste
Evaluate gas cylinders, unknowns & potential explosives
Laboratory and Stockroom cleanouts

## Slide 45: Spill Clean up
When responding to a small chemical or hazardous waste spill,
  REFER SDS for the material’s hazards and
  Potential to react with other materials
Contact OEH&S for spill clean-up assistance when:
  Large spills
  Spills involving extremely hazardous chemicals
  Inadequate ventilation in spill area
  No spill clean-up materials
  Personnel uncomfortable handling clean-up
  If a spilled chemical enters the drain, soil or water body

## Slide 46: When Cleaning a Spill
Consult MSDS & wear proper PPE prior to clean-up.
Spread absorbent around and over liquid’s surface
Collect wet absorbents & transfer them in plastic bucket or bag using dustpan & brush
Label the contents of bucket/bag using yellow waste tags.
Call OEHS for waste pick-up

## Slide 47: Accident management
Dial 911 on campus for emergencies
Call Office of Environmental Health & Safety
    for assistance with spills that you are uncomfortable handling
    to clean up mercury spills
After hours or on weekends call campus police to contact OEHS staff

## Slide 48: Summary
Containers must be in good condition.
The waste placed in the container must be compatible with the container.
Containers must be clearly and legibly labeled with the yellow “Chemical Waste Label”
The label must be firmly attached to the container.
Containers must be placed next to or near the process that generates the waste.
Containers must be kept closed at all times except when adding or removing waste.
Containers must be segregated by hazard class (e.g. acids from bases and flammables).
Containers and area must be inspected at least weekly for leakage.

## Slide 49: Acknowledgement of Training
Click here to acknowledge receipt of training
Contact OEHS at 824-6053 for any questions or
www.uah.edu/oehs